## Slide 1: Status of the APEnet+ project
davide.rossetti@roma1.infn.it
Lattice 2011
Squaw Valley, Jul 10-16, 2011

## Slide 2: Index
GPU accelerated cluster and the APEnet+ interconnect
Requirements from LQCD application(s)
The platform constraints: PCIe, links
Accelerating the accelerator 
Programming model
The RDMA API
CUOS
Future devel

## Slide 3: The APEnet+ History
Custom HPC platform: APE (86), APE100 (94), APEmille (99), apeNEXT (04)
Cluster Interconnect:
  2003-2004: APEnet V3
  2005: APEnet V3+, same HW with RDMA API
  2006-2009: DNP, or APEnet goes embedded
  2011: APEnet V4 aka APEnet+

## Slide 4: Why a GPU cluster today
GPU cluster has:
Very good flops/$ W/$ ratios
Readily available
Developer friendly, same technology from laptop to cluster
Good support from industry
Active developments for LQCD
Missing piece: a good network interconnect

## Slide 5: APEnet+ HW
Logic structure
Test card
Final card
CAVEAT: immature situation, rapidly converging
Very early figures, improving every day
Releasing conservative assumptions
Eg: in a few hours, from 30us to 7us latency

## Slide 6: APEnet+ HW
router
7x7 ports switch
torus
link
torus
link
torus
link
torus
link
torus
link
torus
link
TX/RX FIFOs & Logic
routing logic
arbiter
X+
X-
Y+
Y-
Z+
Z-
PCIe X8 Gen2 core
NIOS II processor
collective communication block
memory controller
DDR3
Module
128@250MHz bus
PCIe X8 Gen2 8@5 Gbps
100/1000 Eth port
Altera Stratix IV
FPGA blocks
  3D Torus, scaling up to thousands of nodes
    packet auto-routing
    6 x 34+34 Gbps links
    Fixed costs: 1 card + 3 cables
  PCIe X8 gen2
    peak BW 4+4 GB/s
  A Network Processor
    Powerful zero-copy RDMA host interface
    On-board processing
    Experimental direct GPU interface
  SW: MPI (high-level), RDMA API (low-level)

## Slide 7: APEnet+ HW
Test Board
Based on Altera development kit
Smaller FPGA
Custom daughter card with 3 link cages
Max link speed is half
APEnet+ final board, 4+2 links
Cable options: copper or fibre

## Slide 8: Requirements from LQCD
Our GPU cluster node:
A dual-socket multi-core CPU
2 Nvidia M20XX GPUs
one APEnet+ card
Our case study:
64^3x128 lattice
Wilson fermions
SP

## Slide 9: Requirements from LQCD
even/odd + γ projection trick Dslash:
  f(L, NGPU) = 1320/2 × NGPU × L3T flops
  r(L, NGPU) = 24/2 × 4 × (6/2 NGPU L2T + x/2 L3) bytes with x=2,2,0 for NGPU=1,2,4
Balance condition*, perfect comp-comm overlap
  f(L, NGPU)/perf(NGPU) = r(L, NGPU)/BW 
  BW(L, NGPU) = perf(NGPU) × r(L, NGPU) / f(L, NGPU)
* Taken from Babich (STRONGnet 2010), from Gottlieb via Homgren

## Slide 10: Requirements from LQCD (2)
For L=T, NGPU=2, perf 1 GPU=150 Gflops sustained:
  BW(L, 2) = 2×150×109 × 24 (6×2+2)L3 / (1320× L4) = 76.3/L GB/s
  14 messages of size m(L) = 24 L3 bytes
2 GPUs per node, at L=32:
  E/O prec. Dslash compute-time is 4.6ms
  BW(L=32) is 2.3 GB/s
  Transmit 14 buffers of 780KB, 320us for each one
  Or 4 KB pkt in 1.7us

## Slide 11: Requirements from LQCD (2)
GPU lattice | GPUs per node | Node lattice | Global lattice | # of nodes | # of GPUs | Req BW GB/2
16ˆ3*16 | 2 | 16ˆ3*32 | 64ˆ3*128 | 256 | 512 | 4.3
16ˆ3*32 | 2 | 16ˆ3*64 | 64ˆ3*128 | 128 | 256 | 4.0
32ˆ3*32 | 2 | 32ˆ3*64 | 64ˆ3*128 | 16 | 32 | 2.1
16ˆ3*32 | 4 | 16ˆ3*128 | 64^3*128 | 64 | 256 | 7.4
32ˆ3*32 | 4 | 32ˆ3*128 | 64^3*128 | 8 | 32 | 3.7
Single 4KB pkt lat is: 1.7us
At PCIe x8 Gen 2 (~ 4 GB/s) speed: 1us
At Link (raw 34Gbps or ~ 3 GB/s) speed: 1.36us
APEnet+ SW + HW pipeline: has ~ 400 ns !?!
Very tight time budget!!!

## Slide 12: The platform constraints
PCIe *:
  One 32bit reg posted write: 130ns
  One regs read: 600ns
  8 regs write: 1.7us
PCIe is a complex beast!
  Far away from processor and memory (on-chip mem ctrl)
  Mem reached through another network (HT or QPI)
  Multiple devices (bridges, bufs, mem ctrl) in between
  Round-trip req (req + reply) ~ 500ns !!!
* Measured with a tight loop and x86 TSC

## Slide 13: A model of pkt flow
Pkt 1
Pkt 1
tlink
tpci
tlink
twire
tsw
tovr
tpci
tovr + 2tsw + tlink + twire
tlink
tpci > tlink
tpci
tsw +twire + tsw = 260ns
router
torus
link
torus
link
torus
link
torus
link
torus
link
torus
link
TX/RX FIFOs & Logic
PCIe X8 Gen2 core
NIOS II processor
collective communication block
memory controller
128@250MHz bus
Altera Stratix IV

## Slide 14: Hard times
Two different traffic patterns:
Exchanging big messages is good
  Multiple consecutive pkts
  Hidden latencies
  Every pkt latency (but the 1st ) dominated by tlink
A classical latency test (ping-pong, single pkt, down to 1 byte payload) is really hard
  Can’t neglect setup and teardown effects
  Hit by full latency every time
  Need very clever host-card HW interface

## Slide 15: GPU support
Some HW features developed for GPU
P2P
Direct GPU

## Slide 16: The traditional flow
Network
CPU
GPU
Director
kernel
calc
CPU memory
GPU memory
transfer

## Slide 17: GPU support: P2P
CUDA 4.0 brings:
  Uniform address space
  P2P among up to 8 GPUs
Joint development with NVidia
  APElink+ acts as a peer
  Can read/write GPU memory
Problems:
  work around current chipset bugs
  exotic PCIe topologies
  PCIe topology on Sandy Bridge Xeon

## Slide 18: P2P on Sandy Bridge

## Slide 19: GPU: Direct GPU access
Specialized APEnet+ HW block
GPU initiated TX
Latency saver for small size messages
SW use: see cuOS slide

## Slide 20: Improved network
APEnet+
CPU
GPU
Director
kernel
CPU memory
GPU memory
transfer
P2P transfer
Direct GPU access

## Slide 21: SW stack
GPU centric programming model

## Slide 22: SW: RDMA API
RDMA Buffer management:
  am_register_buf, am_unregister_buf
  expose memory buffers
  2 types: SBUF use-once, PBUF are targets of RDMA_PUT
  Typically at app init time
Comm primitives:
  Non blocking, async progress
  am_send() to SBUF
  am_put() to remote PBUF via buffer id
  am_get() from remote PBUF (future work)
Event delivery:
  am_wait_event()
  When comm primitives complete
  When RDMA buffers are accessed

## Slide 23: SW: RDMA API
Typical LQCD-like CPU app
Init:
  Allocate buffers for ghost cells
  Register buffers
  Exchange buffers ids
Computation loop:
  Calc boundary
  am_put boundary to neighbors buffers
  Calc bulk
  Wait for put done and local ghost cells written
Same app with GPU
Init:
  cudaMalloc() buffers on GPU
  Register GPU buffers
  Exchange GPU buffer ids
Computation loop:
  Launch calc_bound kernel on stream0
  Launch calc_bulk kernel on stream1
  cudaStreamSync(stream0)
  am_put(rem_gpu_addr)
  Wait for put done and buffer written
  cudaStreamSync(stream1)
Thanks to P2P!

## Slide 24: SW: MPI
OpenMPI 1.5
Apelink BTL-level module
2 protocols based on threshold
  Eager: small message size, uses plain send, async
  Rendezvous: pre-register dest buffer, use RDMA_PUT, need synch
Working on integration of P2P support
  Uses CUDA 4.0 UVA

## Slide 25: SW: cuOS
cuOS = CUDA Off-loaded System services
cuMPI: MPI APIs …
cuSTDIO: file read/write ...
... in CUDA kernels!
Encouraging a different programming model:
  program large GPU kernels
  with few CPU code
  hidden use of direct GPU interface
  need resident blocks (global sync)
cuOS is developed by APE group and is open source
http://code.google.com/p/cuos

## Slide 26: SW: cuOS in stencil computation
using in-kernel MPI (cuOS):
//GPU
__global__ void solver() {
do {
compute_borders();
cuMPI_Isendrecv(boundary, frames);
compute_bulk();
cuMPI_Wait();
local_residue(lres);
cuMPI_Reduce(gres, lres);
} while(gres > eps);
}
// CPU
main() {
...
solver<<<nblocks,nthreads>>>();
cuos->HandleSystemServices();
...
}
traditional CUDA:
//GPU
__global__ void compute_borders(){}
__global__ void compute_bulk(){}
__global__ void reduce(){}
//CPU
main() {
do {
compute_bulk<<<,1>>>();
compute_borders<<<,0>>>();
cudaMemcpyAsync(boundary, 0);
cudaStreamSynchronize(0);
MPI_Sendrecv(boundary, frames);
cudaMemcpyAsync(frames, 0);
cudaStreamSynchronize(0);
cudaStreamSynchronize(1);
local_residue<<<,1>>>();
cudaMemcpyAsync(lres, 1);
cudaStreamSynchronize(1);
MPI_Reduce(gres, lres);
} while(gres > eps);
}

## Slide 27: QUonG reference platform
Today:
  7 GPU nodes with Infiniband for applications development: 2 C1060 + 3 M2050 + S2050
  2 nodes HW devel: C2050 + 3 links card APEnet+
Next steps, green and cost effective system within 2011
  Elementary unit:
      multi-core Xeon (packed in 2 1U rackable system)
      S2090 FERMI GPU system (4 TFlops)
      2 APEnet+ board
  42U rack system:
        60 TFlops/rack peak
        25 kW/rack (i.e. 0.4 kW/TFlops)
        300 k€/rack (i.e. 5 K€/Tflops)

## Slide 28: Status as of Jun 2011
Early prototypes of APEnet+ card
  Due in a few days
  After some small soldering problems
Logic: fully functional stable version
  Can register up to 512 4KB buffers
  Developed on test platform
  OpenMPI ready
Logic: early prototype of devel version
  FPGA processor (32bit 200MHz 2GB RAM)
  Unlimited number and size of buffers (MMU)
  Enabling new developments

## Slide 29: Future works
Goodies from next gen FPGA
  PCIe Gen 3
  Better/faster links
  On-chip processor (ARM)
Next gen GPUs
  NVidia Kepler
  ATI Fusion ?
  Intel MIC ?

## Slide 30: Game over…
Let’s collaborate… we need you!!!
Proposal to people interested in GPU for LQCD
Why don’t me meet together, ½ hour, here in Squaw Valley ?????

## Slide 31
Back up slides

## Slide 32: Accessing card registers through PCIe
spin_lock/unlock: total dt=1300us loops=10000 dt=130ns
spin_lock/unlock_irq: total dt=1483us loops=10000 dt=148ns
spin_lock/unlock_irqsave: total dt=1727us loops=10000 dt=172ns
BAR0 posted register write: total dt=1376us loops=10000 dt=137ns
BAR0 register read: total dt=6812us loops=10000 dt=681ns
BAR0 flushed register write: total dt=8233us loops=10000 dt=823ns
BAR0 flushed burst 8 reg write: total dt=17870us loops=10000 dt=1787ns
BAR0 locked irqsave flushed reg write: total dt=10021us loops=10000 dt=1002ns

## Slide 33: LQCD requirements (3)
Report 2 and 4 GPUS per node
L=16,24,32

## Slide 38: Latency on HW simulator
Chart: APEnet+ Latency (CLK_T = 425 MHZ)
| 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 24576.0 | 28672.0 | 32768.0
APEnet+ Latency | 0.904 | 0.924 | 0.968 | 1.048 | 1.216 | 1.5 | 2.24 | 3.72 | 6.668 | 9.884 | 16.5 | 22.884 | 26.052 | 29.244

## Slide 39: Intel Westmere-EX
Lot’s of caches!!!
Few processing:
4 FP units are probably 1 pixel wide !!!

## Slide 40: NVidia GPGPU
Lot’s of computing units !!!

## Slide 41: So what ?
What are the differences ?
Why should we bother ?
They show different trade-offs !!
And the theory is…..

## Slide 42: Where the power is spent
“chips are power limited and most power is spent moving data around”*
4 cm2 chip
4000 64bit FPU fit
Moving 64bits on chip == 10FMAs
Moving 64bits off chip == 20FMAs
*Bill Dally, Nvidia Corp. talk at SC09

## Slide 43: So what ?
What are the differences?
Why should we bother?
Today: at least a factor 2 in perf/price ratio
Tomorrow: CPU & GPU converging, see current ATI Fusion

## Slide 44: With latest top GPUs…
Dell PowerEdge C410x

## Slide 45: Executive summary
GPUs are prototype of future many-core arch (MIC,…)
Good $/Gflops and $/W
Increasingly good for HEP theory groups (LQCD,…)
Protect legacy:
  Run old codes on CPU
  Slowly migrate to GPU

## Slide 46: A first exercise
Today needs: lots of MC
Our proposal: GPU accelerated MC
Unofficially: interest by Nvidia …
NVidia
CERN
Intel MIC
Closing the loop 

## Slide 47: Final question
A GPU and Network accelerated cluster:
Could it be the prototype of the SuperB computing platform ?